## Slide 1
IEEE WCCI 2026 · MAASTRICHT, NETHERLANDS · 21–26 JUNE 2026 · POSTER SESSION
Edge-Cell Graph Encoding and Fixed-Point Arithmetic for FPGA Growing Neural Gas
Bringing unsupervised learning down to the embedded level
Teuku Zikri Fatahillah1 · Raditya Artha Rochmanto1,2 · Achmad Fahrul Aji1,2
Anhar Risnumawan1,3 · Chyan Zheng Siow1,4 · Naoyuki Kubota1
1 Tokyo Metropolitan University, Japan · 2 Politeknik Negeri Semarang, Indonesia
3 Politeknik Elektronika Negeri Surabaya, Indonesia · 4 Changsha Cultural and Creative Arts Vocational College, China
CODE & DATA
github.com/tzf230201/fpga_gng
−41%
smaller graph-state memory (2,000 B → 1,180 B)
~625 µs
deterministic latency / sample (≈1,600 / s)
38%
LUT used on a 9K FPGA — 62% headroom left
1 · Motivation & Problem
Micro-UAV swarms and field robots need on-board unsupervised adaptation — streaming raw data to the cloud is impractical. Learning must run locally, with bounded memory and deterministic timing .
Growing Neural Gas (GNG) learns topology incrementally, sample-by-sample, without labels — ideal for streaming data. But classic GNG clashes with small FPGAs:
Topological mapping in action: a robot explores its surroundings (left) while GNG incrementally builds a graph mirroring the free-space topology (right) — applications like this need adaptation to run on the device itself: payload-, power-, and link-constrained.
▸
Dense adjacency is O(N²): a 40×40 8-bit matrix = 1,600 B — it dominates the BRAM budget of a sub-10K-LUT device.
▸
Floating-point needs FPU blocks or slow iterative units — integer-only datapaths map cleanly to LUTs and DSPs.
▸
Prior FPGA self-organizing work targets SOMs with static lattices — GNG's per-iteration edge insert/age/prune on a variable graph is the hard part.
2 · Method Overview
A fully integer, single-FSM GNG engine in synthesizable VHDL on the Sipeed Tang Nano 9K (Gowin GW1NR-9C) — no soft-core CPU, no FPU, no PLL.
i
Edge-cell encoding — upper-triangular half-adjacency with 8-bit age+1 cells: 780 B vs 1,600 B edge storage.
ii
Shift-based Q8/Q16 learning rates — every adaptation step is one multiply + shift, single DSP cycle.
iii
Fused NB_SCAN pass — error decay + edge aging + neighbor movement + pruning in one sequential sweep; no separate full-array decay pass.
iv
Per-node degree counters — O(Nmax ) isolated-node detection without scanning the edge array.
3 · GNG Loop
①
Find winner s₁ = argminᵢ ‖ξ − wᵢ‖² and runner-up s₂.
②
Accumulate winner error; move s₁ toward ξ by εw.
③
Age edges of s₁; move its neighbors by εn; prune edges past Amax.
④
Connect (s₁, s₂) with age 0; decay all errors by β.
⑤
Every λ samples: insert a node between the max-error node and its worst neighbor; split errors by α.
CORE METHOD
4 · Edge-Cell Encoding
Edges are undirected, so store only the upper triangle of the adjacency — one byte per node pair, coding presence and age together :
node j →
← node i
0
1
2
3
4
5
0
3
1
0
0
0
1
0
7
0
0
2
2
5
0
3
0
1
4
4
5
cell = age + 1 (stored edge)
cell = 0 (no edge)
lower triangle + diagonal — never stored
Half-adjacency indexing — flatten the 2D upper triangle into one 1D array, row by row:
0
0,1
1
0,2
2
0,3
3
0,4
4
0,5
5
1,2
6
1,3
7
1,4
8
1,5
9
2,3
10
2,4
11
2,5
12
3,4
13
3,5
14
4,5
idx(i, j) =
i (2Nmax − i − 1)
2
+ (j − i − 1)
(1,3) → cell 6
Implementation
Node
Edge
Total
Dense adjacency (baseline)
400 B
1,600 B
2,000 B
Edge-cells (proposed)
400 B
780 B
1,180 B
−51.25% edge storage · −41% total graph state at Nmax = 40 — freeing BRAM for application logic.
5 · Fixed-Point Arithmetic
Integer-only datapath —
No floating-point unit. The whole engine runs on a Tang Nano 9K @ 27 MHz
(single FSM, 3 BRAMs, UART 1 Mbit/s).
Tang Nano 9K · GW1NR-9C
Coordinate representation — 16-bit signed integers in [−1000, 1000] after min-max normalization:
xnorm =
(
x − xmin
xmax − xmin
)
· 2s − s ,
s = 1000
80-bit node word — one BRAM entry per node:
x [16]
y [16]
deg [8]
err [32]
Squared-distance unit — maps directly onto a 9×9 DSP multiplier, overflow-free:
Δx = ξx − xn , Δy = ξy − yn 17-bit signed
d² = Δx² + Δy² 35-bit unsigned
Parametric learning rates — one multiply + shift each (single DSP cycle):
Winner (Q8)
Δx
s₁
= ⌊
77 (ξx − xs₁)
2⁸
⌋
εw ≈ 0.301
Neighbor (Q16)
Δx
n
= ⌊
66 (ξx − xn)
2¹⁶
⌋
εn ≈ 0.001
Multiplierless error decay
err −= err ≫ 8
no multiplier (β ≈ 0.9961)
Fused update: winner move, edge aging, neighbor move, error decay & pruning all run in one NB_SCAN sweep — independent per-edge ops, parallelizable on FPGA.
6 · Results — It Fits, and It Learns
38%
LUT · 3,205/8,640
22%
FF · 1,408/6,693
24%
BSRAM · 6/26
50%
DSP · 5/10
Place-and-route on Gowin GW1NR-LV9QN88PC6 (Gowin EDA V1.9.12.01) — 62% LUT and 76% BRAM headroom remain for application logic.
Topologies learned on the FPGA , streamed via UART snapshots. Left: Two Moons (epoch 32). Right: Concentric Circles (epoch 64). 100 samples each, Nmax = 40.
Two Moons (final)
QE 0.146 · TE 0.01
Concentric Circles (final)
QE 0.196 · TE 0.07
QE (quantization error) drops steadily on both datasets and TE (topological error) stays near zero — the integer engine matches floating-point GNG quality. TE drifts slightly on Circles only after N max saturates.
7 · Deterministic Real-Time Throughput
~625 µs
per sample
~16.9k
cycles @ 27 MHz
~1,600
samples / s
Measured from an on-chip 32-bit cycle counter embedded in every debug frame — Two Moons: 16,852 cycles (624.1 µs); Circles: 16,931 cycles (627.1 µs). Latency is dominated by the two O(N max) BRAM scans — bounded and near-identical across datasets .
8 · Takeaway & Future Work
Self-organizing clustering with dynamic topology is feasible on a sub-10K-LUT FPGA — when memory layout and arithmetic format are treated as first-class design concerns. Bounded state + incremental updates make this a hardware substrate for continual learning at the edge .
PROSPECTIVE APPLICATIONS
Aerial robot
Bio-inspired robot
Drone swarm
Exploration robot
Streaming sensor input — adapt continuously without restart
Pipelined O(log N) winner-search tree
Q-format precision via VHDL generics
Multi-stream on-board unsupervised mapping
Selected References
[1] B. Fritzke, “A growing neural gas network learns topologies,” NeurIPS, 1994.
[2] T. Kohonen, “Self-organized formation of topologically correct feature maps,” Biol. Cybern. , 1982.
[8] J. Holmström, “Growing neural gas with utility,” Neural Networks, 2002.
[16] P. Coelho et al., “FPGA implementation of self-organizing maps using fixed-point arithmetic,” J. Signal Process. Syst. , 2020.
[25] Piyasena et al., dynamically growing SO network (GWR-like) on FPGA for lifelong learning at the edge.
[26] Firmli et al., compressed sparse row (CSR++) for low-degree-graph memory reduction.
Supported by the Japan Science and Technology Agency (JST), Moonshot R&D Program, grant JPMJMS2034.
[email protected]
FPGA
Parameter
Value
Hardware mapping
Nₘₐₓ (max nodes)
40
node BRAM depth
Aₘₐₓ (max edge age)
50
A_MAX_STORED = 51
λ (insertion period)
100
lambda_cnt counter
εw (winner lr)
≈ 0.301
EPS_WIN_Q8 = 77, ≫ 8
εn (neighbor lr)
≈ 0.001
EPS_N_Q16 = 66, ≫ 16
α (error split)
0.5
INS_ALPHA_SHIFT = 1
β (error decay)
≈ 0.9961
ERR_DECAY_SHIFT = 8
ERR_SHIFT (acc. scale)
4
d² ≫ 4 before accum.
Sample input ξ
SAMPLE
↓
Find winner s₁, runner-up s₂
WIN_SCAN
↓
FUSED IN ONE SWEEP · UPDATE + NB_SCAN
Σ accumulate s₁ error
Move s₁ toward ξ (εw)
Age s₁ edges + prune
Move neighbors (εn)
independent per-edge ops → parallelizable on FPGA
↓
Connect (s₁, s₂) · decay errors (β)
CONNECT
↓
Insert node @ λ · remove old/isolated
INSERT
↻ repeat until termination
Each BRAM read-modify-write takes ≥ 3 cycles → deterministic, bounded per-sample latency .
Many deep learning systems rely on labels, pretraining, or task-specific prior knowledge. In unseen or changing environments, robots may need to discover structure directly from streaming sensory data. Unsupervised topology learning methods such as SOM and GNG can learn online without labels.