## Slide 1
Edge-Cell Graph Encoding and Fixed-Point Arithmetic for FPGA Growing Neural Gas
Bringing Online Topology Learning Down to Embedded FPGA
Teuku Zikri Fatahillah1 · Raditya Artha Rochmanto1,2 · Achmad Fahrul Aji1,2 · Anhar Risnumawan1,3 · Chyan Zheng Siow1,4 · Naoyuki Kubota1
1 Tokyo Metropolitan University, Japan 2 Politeknik Negeri Semarang, Indonesia 3 Politeknik Elektronika Negeri Surabaya, Indonesia 4 Changsha CCAVC, China
June 21–26, 2026
−41%
Graph-State Memory
(2,000 B → 1,180 B)
~625 µs
Latency per Sample
(@ 27 MHz)
38%
LUT Utilization
(of 8,640 LUTs)
~1,600
Samples / Second
(Throughput)
1 · MOTIVATION & PROBLEM
Many deep-learning systems rely on labels, pre-training, or task-specific priors .
In unseen or changing environments, robots must discover structure directly from streaming sensory data.
Unsupervised topology learners like SOM and GNG learn online without labels.
⚠ But deploying GNG on tiny FPGAs is challenging:
① Dynamic topology on static hardware
GNG continually creates, ages, and removes edges — creating irregular memory access and control-flow pressure on a small FPGA.
② Dense adjacency wastes graph memory
An N×N adjacency matrix at Nmax =40 alone consumes 1,600 B before any node coordinate is stored.
③ Floating-point units are too costly
Per-sample distance and learning-rate updates increase area and latency, limiting usefulness on a sub-10K-LUT FPGA.
Design target
A bounded-memory, integer-only GNG accelerator that preserves dynamic topology while fitting the Tang Nano 9K resource envelope.
2 · METHOD OVERVIEW
What is GNG? Growing Neural Gas is a self-organizing clustering algorithm that incrementally learns a graph approximating the data distribution — discovering both prototype nodes and their topology online, without labels.
① Fused Update Pass
Error decay, edge aging, neighbor movement, and pruning combined in one NB_SCAN sweep — eliminating a separate full-array decay pass.
• While stepping node n: decay error, probe edge_cell[idx(s1,n)]
• If active edge: age it, move neighbor, prune if over-age
• Per-node degree counters enable isolated-node detection with no extra scan
FSM PIPELINE — PER INPUT SAMPLE
SAMPLE
fetch input ξ
↓
WIN_SCAN
find nearest s₁, s₂
↓
UPDATE
winner error + Q8 move
↓
NB_SCAN — FUSED
decay error · probe edge_cell · age / prune · move neighbor
one Nmax scan replaces the separate decay + neighbor passes
↓
CONNECT
reset edge (s₁, s₂) age = 0
↓
INSERT
every λ — split max-error edge
② Edge-Cell Encoding
One byte per node pair stores age+1 (0 = no edge). At Nmax =40: edge storage 1,600 B → 780 B (−51%).
③ Fixed-Point Arithmetic
Integer-only datapath — no FPU. Coordinates: 16-bit signed integers in [−1000, 1000] after min-max normalization.
Squared distance (17-bit → 35-bit, DSP 9×9):
Δx = ξx − xn, Δy = ξy − yn
d² = Δx² + Δy² (overflow-free)
Winner adaptation (Q8, εw ≈ 0.301):
Δxs1 = ⌊EPS_WIN_Q8 × (ξx − xs1) » 8⌋
EPS_WIN_Q8 = 77 → εw = 77/256 ≈ 0.301
Neighbor adaptation (Q16, εn ≈ 0.001):
Δxn = ⌊EPS_N_Q16 × (ξx − xn) » 16⌋
EPS_N_Q16 = 66 → εn = 66/65536 ≈ 0.001
Error decay (no multiplier, β ≈ 0.9961):
errn -= errn » ERR_DECAY_SHIFT
ERR_DECAY_SHIFT = 8 → β = 1 − 2⁻⁸ ≈ 0.9961
Param
Value
HW mapping
Nₘₐₓ
40
node BRAM depth
Aₘₐₓ
50
A_MAX_STORED = 51
λ
100
lambda_cnt counter
εw
≈ 0.301
EPS_WIN_Q8 = 77, ≫ 8
εn
≈ 0.001
EPS_N_Q16 = 66, ≫ 16
α
0.5
INS_ALPHA_SHIFT = 1
β
≈ 0.9961
ERR_DECAY_SHIFT = 8
3 · FPGA ARCHITECTURE
GNG Engine — Single FSM
Nearest-Node Search
Weight Update
Edge Update & Aging
Node Insertion / Deletion
Fixed-Point Arithmetic (Q8 / Q16)
Sipeed Tang Nano 9K Gowin GW1NR-9C · 27 MHz
Node, edge & dataset BRAMs · UART 1 Mbit/s host link · deterministic ≥ 3-cycle BRAM access.
NO LABELS. NO CLOUD. STILL LEARNING.
Small FPGAs can learn topology online.
Streaming Sensory Data
→
Integer FPGA Engine
→
Learned Topology (Growing Graph)
Unsupervised Topology Learning (GNG)
Integer-Only Fixed-Point (Q8 / Q16)
Memory-Efficient Edge-Cell Encoding
Online structure discovery, without labels, without cloud, on a tiny FPGA.
EDGE-CELL ENCODING — HALVES GRAPH STORAGE
Dense Adjacency O(N²)
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1,600 B
full N×N matrix (baseline)
−51%
edge storage
→
Edge-Cell Half-Adj. O(E)
0
2
0
0
0
0
0
0
3
0
0
1
0
0
1
0
0
0
0
2
0
0
0
1
0
0
3
0
780 B
upper triangle, age+1 (proposed)
Total graph state
2,000 B → 1,180 B
−41%
SCAN FOR EVERYTHING
Paper · Poster · Slides · Source Code
github.com/tzf230201/fpga_gng
4 · MEMORY COMPARISON
Component
Baseline
Proposed
Saving
Node array
400
400
—
Edge Memory
1,600
780
−51.25
Total graph state
2,000
1,180
−41.0
5 · FPGA RESOURCE UTILIZATION
Resource
Used
Avail.
Util.
LUT
3,205
8,640
38%
FF
1,408
6,693
22%
BSRAM
6
26
24%
DSP
5
10
50%
6 · LEARNING PERFORMANCE (QE / TE)
Two Moons
Epoch
Nodes
Edges
QE
TE
16
19
22
0.4750
0.00
32
35
33
0.1832
0.00
48
40
37
0.1461
0.00
64
40
34
0.1455
0.01
Concentric Circles
Epoch
Nodes
Edges
QE
TE
16
19
33
0.6964
0.00
32
35
36
0.2592
0.00
48
40
40
0.2000
0.04
64
40
39
0.1960
0.07
7 · LEARNED TOPOLOGIES & TRAINING DYNAMICS
Two Moons — Epoch 32
Concentric Circles — Epoch 64
Two Moons — Training Dynamics (32 epochs)
Concentric Circles — Training Dynamics (64 epochs)
8 · REAL-TIME THROUGHPUT
Per-sample latency ~625 µs, measured from the on-chip 32-bit cycle counter
Dataset
Cycles
µs
Samp/s
Total s
Two Moons
16,852
624.1
1,602
5.40
Concentric Circles
16,931
627.1
1,595
5.72
PROSPECT APPLICATIONS
Aerial robot
Bio-inspired robot
Swarm robots
Exploration robot
Infrastructure inspection
Supported by the Japan Science and Technology Agency (JST), Moonshot R&D Program, grant JPMJMS2034.
[email protected]