## Slide 1
Edge-Cell Graph Encoding and Fixed-Point Arithmetic for FPGA Growing Neural Gas
Integer-only online topology learning on a sub-10K-LUT FPGA
Teuku Zikri Fatahillah1 · Raditya Artha Rochmanto1,2 · Achmad Fahrul Aji1,2 · Anhar Risnumawan1,3 · Chyan Zheng Siow1,4 · Naoyuki Kubota1
1 Tokyo Metropolitan University, Japan · 2 Politeknik Negeri Semarang, Indonesia · 3 PENS, Indonesia · 4 Changsha CCAVC, China
IEEE WCCI 2026 Maastricht
-41%
total graph-state memory
2,000 B -> 1,180 B
~625 us
deterministic latency
~16.9k cycles @ 27 MHz
38%
LUT utilization
3,205 / 8,640 LUTs
~1,600/s
online throughput
UART-measured FPGA snapshots
1 · Problem & Motivation
Edge robots need on-board unsupervised adaptation.
Streaming raw sensor data to the cloud is often impractical under intermittent links and latency limits.
GNG learns a topology incrementally, but dynamic edges and floating point are expensive on tiny FPGAs.
The target is bounded memory, deterministic per-sample time, and an integer-only datapath.
Tang Nano 9K
Unstructured field scene -> integer FPGA engine -> online topology graph
2 · Contributions in the Paper
Synthesized GNG engine on Gowin GW1NR-9C with no CPU, no FPU, and no PLL.
Edge-cell graph storage: upper triangle only, one 8-bit age+1 cell per possible undirected edge.
Q8/Q16 shift-scaled learning rates mapped to DSP-friendly multiply-and-shift updates.
Winner-indexed fused NB_SCAN combines error decay, edge aging, neighbor movement, and pruning.
No soft-core CPU
FSM datapath
No FPU
Q8/Q16 shifts
No dynamic memory
fixed BRAM arrays
3 · FPGA Architecture
Single-clock FSM at 27 MHz with BRAM-mapped state.
UART input
100-sample dataset ROM
WIN_SCAN
nearest s1, runner-up s2
UPDATE
winner error + Q8 move
NB_SCAN
node BRAM + edge BRAM RMW
CONNECT / INSERT
degree counters + split edge
DBG/SNAP
cycle counter + topology stream
Node, edge, and dataset BRAMs use synchronous read-modify-write access; each sequence costs at least 3 cycles.
4 · GNG Loop and Fused NB_SCAN
Paper-aligned FSM sequence per input sample
SAMPLE
fetch input xi
WIN_SCAN
find s1 and s2
UPDATE
err_s1 += d2 >> ERR_SHIFT; move s1 by EPS_WIN_Q8
NB_SCAN
decay err_n; probe edge_cell[idx(s1,n)]
ACTIVE EDGE
age/prune edge; move neighbor by EPS_N_Q16
CONNECT
reset edge(s1,s2) age; update degree counters
INSERT / SNAP
every lambda split max-error edge; stream UART snapshots
Why fused?
Canonical GNG separates global error decay from winner-neighbor edge updates.
The FPGA already scans all node slots around s1, so decay is folded into the same NB_SCAN.
Per-node degree counters detect isolated nodes without a second full edge-array scan.
Hardware invariant
Only fixed-capacity arrays are used: node state is stored once, edge state is stored once, and dynamic topology is expressed by age+1 cells and degree counters. This keeps memory bounded even as GNG rewires.
State
BRAM word
Role
node
x,y,deg,err
coordinates + degree + error
edge
age+1
0 = inactive; v>0 = age v-1
dataset
x,y sample
100-entry on-chip input set
5 · Edge-Cell Encoding
Flatten only the upper triangle of an undirected graph.
node j ->
<- node i
0
1
2
3
4
5
0
3
1
0
0
0
1
0
7
0
0
2
2
5
0
3
0
1
4
4
5
cell = age + 1
0 means no edge
v > 0 means true age = v - 1
Half-adjacency indexing, row by row
0
0,1
1
0,2
2
0,3
3
0,4
4
0,5
5
1,2
6
1,3
7
1,4
8
1,5
9
2,3
10
2,4
11
2,5
12
3,4
13
3,5
14
4,5
idx(i,j) = i(2Nmax - i - 1)/2 + (j - i - 1)
(1,3) -> cell 6
Example uses Nmax = 6: 1(12 - 1 - 1)/2 + (3 - 1 - 1) = 5 + 1 = 6
Dense matrix
Edge-cell array
40 x 40 x 8-bit = 1,600 B
->
40 x 39 / 2 bytes = 780 B
51.25% less edge storage; total graph state drops 2,000 B -> 1,180 B.
This matches the paper's fixed-capacity allocation: graph growth and rewiring do not allocate memory dynamically; they only update existing node and edge BRAM cells.
Presence + age
one byte encodes both
Deterministic address
13-bit BRAM index at Nmax=40
Degree counters
isolated nodes need no edge scan
6 · Fixed-Point Arithmetic
Integer-only datapath
Coordinates are 16-bit signed integers in [-1000, 1000] after min-max normalization.
Coordinate representation
x_norm = ((x - x_min) / (x_max - x_min)) * 2S - S, S = 1000
80-bit node word
x [16]
y [16]
deg [8]
err [32]
Squared-distance unit
dx = xi_x - x_n, dy = xi_y - y_n d2 = dx^2 + dy^2 // 17-bit signed -> 35-bit unsigned err_s1 += d2 >> ERR_SHIFT
Winner adaptation, Q8
Delta x_s1 = floor(EPS_WIN_Q8 * (xi_x - x_s1) / 2^8) Delta y_s1 = floor(EPS_WIN_Q8 * (xi_y - y_s1) / 2^8)
Neighbor adaptation, Q16
Delta x_n = floor(EPS_N_Q16 * (xi_x - x_n) / 2^16) Delta y_n = floor(EPS_N_Q16 * (xi_y - y_n) / 2^16)
Multiplierless error decay
err_n = err_n - (err_n >> ERR_DECAY_SHIFT) beta approx 1 - 2^-8 = 0.9961
Parameter
Value
Hardware mapping
Nmax
40
node BRAM depth
Amax
50
A_MAX_STORED = 51
lambda
100
lambda counter
eps_w
~0.301
EPS_WIN_Q8 = 77, >> 8
eps_n
~0.001
EPS_N_Q16 = 66, >> 16
alpha
0.5
INS_ALPHA_SHIFT = 1
beta
~0.9961
ERR_DECAY_SHIFT = 8
Where 77 and 66 come from
EPS_Q = round(epsilon * 2^Q). The implementation targets a winner rate near 0.3 and a neighbor rate near 0.001, so EPS_WIN_Q8 = round(0.301 * 256) = 77 and EPS_N_Q16 = round(0.001 * 65536) = 66.
Interpretation
The fixed-point approximation is not exact, but the paper reports low final QE/TE on both datasets, so the hardware-friendly rates are acceptable for the evaluated benchmarks.
7 · Fits on a 9K FPGA
Place-and-route on Gowin GW1NR-LV9QN88PC6
Resource
Used
Avail.
Util.
LUT
3,205
8,640
38%
FF
1,408
6,693
22%
BSRAM
6
26
24%
DSP
5
10
50%
Memory
Baseline
Proposed
Saving
Node array
400 B
400 B
-
Edge memory
1,600 B
780 B
-51.25%
Total graph
2,000 B
1,180 B
-41.0%
The design retains 62% LUT and 76% BRAM headroom for application logic.
8 · Learning Quality
Final FPGA snapshots preserve the target topology.
Two Moons, epoch 32
QE 0.1832, TE 0.00
Concentric Circles, epoch 64
QE 0.1960, TE 0.07
The paper reports QE decreasing on both datasets. TE stays near zero during growth; Circles drifts after saturation because the fixed Nmax graph cannot insert more nodes across the inter-ring gap.
Dataset
Epoch
Nodes
Edges
QE
TE
Two Moons
32
35
33
0.1832
0.00
Two Moons
64
40
34
0.1455
0.01
Circles
32
35
36
0.2592
0.00
Circles
64
40
39
0.1960
0.07
Two Moons training dynamics
node/edge growth, QE convergence, TE
Concentric Circles training dynamics
64 epochs after Nmax saturation
9 · Deterministic Real-Time Throughput
Measured directly from the FPGA cycle counter embedded in DBG frames.
Dataset
Cycles
us
Samples/s
Total s
Two Moons
16,852
624.1
1,602
5.40
Circles
16,931
627.1
1,595
5.72
~1,600 samples/s with bounded per-sample latency
10 · Takeaway and Future Work
Self-organizing clustering with dynamic topology is feasible on a sub-10K-LUT FPGA when memory layout and arithmetic format are co-designed.
Current evaluation: static 2D benchmarks; streaming non-stationary data remains future work.
Next: parallel winner-search tree to reduce O(Nmax) latency toward O(log Nmax).
Next: configurable Q-format constants and multi-stream sensor input.
Target deployment: continual topology learning on low-power, memory-constrained robots/devices.
Code, poster, slides, and data
github.com/tzf230201/fpga_gng
Prospective Edge-Robotics Applications
Lightweight flapping robot
payload-limited topology mapping
Bio-inspired robot
strict body and actuator constraints
Swarm robot
distributed intelligence, low memory
Long-term exploration robot
low power, adaptive autonomy
Infrastructure inspection
narrow spaces, local computation
Supported by the Japan Science and Technology Agency (JST), Moonshot R&D Program, grant JPMJMS2034.
[email protected]