## Slide 1
IEEE WCCI 2026 · MAASTRICHT, NETHERLANDS · 21–26 JUNE 2026 · POSTER SESSION
Edge-Cell Graph Encoding and Fixed-Point Arithmetic for FPGA Growing Neural Gas
Bringing unsupervised learning down to the embedded level
Teuku Zikri Fatahillah1 · Raditya Artha Rochmanto1,2 · Achmad Fahrul Aji1,2
Anhar Risnumawan1,3 · Chyan Zheng Siow1,4 · Naoyuki Kubota1
1 Tokyo Metropolitan University, Japan · 2 Politeknik Negeri Semarang, Indonesia
3 Politeknik Elektronika Negeri Surabaya, Indonesia · 4 Changsha Cultural and Creative Arts Vocational College, China
CODE & DATA
github.com/tzf230201/fpga_gng
−41%
smaller graph-state memory (2,000 B → 1,180 B)
~625 µs
deterministic latency / sample (≈1,600 / s)
38%
LUT used on a 9K FPGA — 62% headroom left
1 · Motivation & Problem
Micro-UAV swarms and field robots need on-board unsupervised adaptation — streaming raw data to the cloud is impractical. Learning must run locally, with bounded memory and deterministic timing .
Growing Neural Gas (GNG) learns topology incrementally, sample-by-sample, without labels — ideal for streaming data. But classic GNG clashes with small FPGAs:
Topological mapping in action: a robot explores its surroundings (left) while GNG incrementally builds a graph mirroring the free-space topology (right) — applications like this need adaptation to run on the device itself: payload-, power-, and link-constrained.
▸
Dense adjacency is O(N²): a 40×40 8-bit matrix = 1,600 B — it dominates the BRAM budget of a sub-10K-LUT device.
▸
Floating-point needs FPU blocks or slow iterative units — integer-only datapaths map cleanly to LUTs and DSPs.
▸
Prior FPGA self-organizing work targets SOMs with static lattices — GNG's per-iteration edge insert/age/prune on a variable graph is the hard part.
2 · Method Overview
A fully integer, single-FSM GNG engine in synthesizable VHDL on the Sipeed Tang Nano 9K (Gowin GW1NR-9C) — no soft-core CPU, no FPU, no PLL.
i
Edge-cell encoding — upper-triangular half-adjacency with 8-bit age+1 cells: 780 B vs 1,600 B edge storage.
ii
Shift-based Q8/Q16 learning rates — every adaptation step is one multiply + shift, single DSP cycle.
iii
Fused NB_SCAN pass — error decay + edge aging + neighbor movement + pruning in one sequential sweep; no separate full-array decay pass.
iv
Per-node degree counters — O(Nmax ) isolated-node detection without scanning the edge array.
3 · GNG Loop & Parameters
①
Find winner s₁ = argminᵢ ‖ξ − wᵢ‖² and runner-up s₂.
②
Accumulate winner error; move s₁ toward ξ by εw.
③
Age edges of s₁; move its neighbors by εn; prune edges past Amax.
④
Connect (s₁, s₂) with age 0; decay all errors by β.
⑤
Every λ samples: insert a node between the max-error node and its worst neighbor; split errors by α.
Parameter
Value
Hardware mapping
Nₘₐₓ (max nodes)
40
node BRAM depth
Aₘₐₓ (max edge age)
50
A_MAX_STORED = 51
λ (insertion period)
100
lambda_cnt counter
εw (winner lr)
≈ 0.301
EPS_WIN_Q8 = 77, ≫ 8
εn (neighbor lr)
≈ 0.001
EPS_N_Q16 = 66, ≫ 16
α (error split)
0.5
INS_ALPHA_SHIFT = 1
β (error decay)
≈ 0.9961
ERR_DECAY_SHIFT = 8
ERR_SHIFT (acc. scale)
4
d² ≫ 4 before accum.
CORE METHOD
4 · Edge-Cell Encoding
Edges are undirected, so store only the upper triangle of the adjacency — one byte per node pair, coding presence and age together :
node j →
node i →
0
1
2
3
4
5
0
3
1
0
0
0
1
0
7
0
0
2
2
5
0
3
0
1
4
4
5
cell = age + 1 (stored edge)
cell = 0 (no edge)
lower triangle + diagonal — never stored
Half-adjacency indexing — flatten the 2D upper triangle into one 1D array, row by row:
0
0,1
1
0,2
2
0,3
3
0,4
4
0,5
5
1,2
6
1,3
7
1,4
8
1,5
9
2,3
10
2,4
11
2,5
12
3,4
13
3,5
14
4,5
idx(i, j) =
i (2Nmax − i − 1)
2
+ (j − i − 1)
(1,3) → cell 6
Implementation
Node
Edge
Total
Dense adjacency (baseline)
400 B
1,600 B
2,000 B
Edge-cells (proposed)
400 B
780 B
1,180 B
−51.25% edge storage · −41% total graph state at Nmax = 40 — freeing BRAM for application logic.
5 · Fixed-Point Arithmetic
Integer-only datapath — no floating-point unit. The whole engine runs on a Tang Nano 9K @ 27 MHz (single FSM, 3 BRAMs, UART 1 Mbit/s).
Tang Nano 9K · GW1NR-9C
Coordinate representation — 16-bit signed integers in [−1000, 1000] after min-max normalization:
xnorm =
(
x − xmin
xmax − xmin
)
· 2s − s ,
s = 1000
80-bit node word — one BRAM entry per node:
x [16]
y [16]
deg [8]
err [32]
Squared-distance unit — maps directly onto a 9×9 DSP multiplier, overflow-free:
Δx = ξx − xn , Δy = ξy − yn 17-bit signed
d² = Δx² + Δy² 35-bit unsigned
Parametric learning rates — one multiply + shift each (single DSP cycle):
Winner (Q8)
Δx
s₁
= ⌊
77 (ξx − xs₁)
2⁸
⌋
εw ≈ 0.301
Neighbor (Q16)
Δx
n
= ⌊
66 (ξx − xn)
2¹⁶
⌋
εn ≈ 0.001
Multiplierless error decay
err −= err ≫ 8
no multiplier (β ≈ 0.9961)
Fused update: winner move, edge aging, neighbor move, error decay & pruning all run in one NB_SCAN sweep — independent per-edge ops, parallelizable on FPGA.
6 · Results — It Fits, and It Learns
38%
LUT · 3,205/8,640
22%
FF · 1,408/6,693
24%
BSRAM · 6/26
50%
DSP · 5/10
Place-and-route on Gowin GW1NR-LV9QN88PC6 (Gowin EDA V1.9.12.01) — 62% LUT and 76% BRAM headroom remain for application logic.
Topologies learned on the FPGA , streamed via UART snapshots. Left: Two Moons (epoch 32). Right: Concentric Circles (epoch 64). 100 samples each, Nmax = 40.
Two Moons (final)
QE 0.146 · TE 0.01
Concentric Circles (final)
QE 0.196 · TE 0.07
QE (quantization error) drops steadily on both datasets and TE (topological error) stays near zero — the integer engine matches floating-point GNG quality. TE drifts slightly on Circles only after N max saturates.
7 · Deterministic Real-Time Throughput
~625 µs
per sample
~16.9k
cycles @ 27 MHz
~1,600
samples / s
Measured from an on-chip 32-bit cycle counter embedded in every debug frame — Two Moons: 16,852 cycles (624.1 µs); Circles: 16,931 cycles (627.1 µs). Latency is dominated by the two O(N max) BRAM scans — bounded and near-identical across datasets .
8 · Takeaway & Future Work
Self-organizing clustering with dynamic topology is feasible on a sub-10K-LUT FPGA — when memory layout and arithmetic format are treated as first-class design concerns. Bounded state + incremental updates make this a hardware substrate for continual learning at the edge .
PROSPECTIVE APPLICATIONS
Aerial robot
Bio-inspired robot
Drone swarm
Exploration robot
Streaming sensor input — adapt continuously without restart
Pipelined O(log N) winner-search tree
Q-format precision via VHDL generics
Multi-stream on-board unsupervised mapping
Selected References
[1] B. Fritzke, “A growing neural gas network learns topologies,” NeurIPS, 1994.
[2] T. Kohonen, “Self-organized formation of topologically correct feature maps,” Biol. Cybern. , 1982.
[8] J. Holmström, “Growing neural gas with utility,” Neural Networks, 2002.
[16] P. Coelho et al., “FPGA implementation of self-organizing maps using fixed-point arithmetic,” J. Signal Process. Syst. , 2020.
[25] Piyasena et al., dynamically growing SO network (GWR-like) on FPGA for lifelong learning at the edge.
[26] Firmli et al., compressed sparse row (CSR++) for low-degree-graph memory reduction.
Supported by the Japan Science and Technology Agency (JST), Moonshot R&D Program, grant JPMJMS2034.
[email protected]